## Slide 1: QUS: Scatterer Size
BME 844 – HW 7
Will Long

## Slide 2
Identifying structures potentially responsible for scattering at clinically relevant frequencies

## Slide 3
Study specific scattering sources in kidney, lymph nodes, blood, and breast
Differentiation and grading of breast tumors

## Slide 4: Faran Model
Frequency dependent scattering
  For a >> λ, interface with f0, i.e. frequency independent
  For a << λ, Rayleigh scatterers with frequency dependence of f4
Size of scatterers between these extremes can be inferred from properties of backscattered waves
Changes in backscatter coefficient with frequency give an indication of scatterer size

## Slide 5: Backscatter Coefficients
Normalized power spectral density of echo signal over 12 dB bandwidth
Normalization, accounts for the area of transducer aperture, axial length of range gated volume, as well as the distance of the gated volume from the transducer
Divided by f4 term (i.e. normalized by small scatterer condition a << λ) and scaled
  Any deviation in frequency dependence from 1 is thus attributed to the scatterer size

## Slide 6: Form Factor Modeling
Comparison of measured backscatter data to scattering model, i.e. form factor function
  Describes the frequency dependence of backscatter (power spectrum)
  Comparison to echo backscatter data to find matching form factor function and corresponding scatterer size
    Matching form factor determined via e.g. least-squares methods (minimum averaged squared deviation of log-difference function)
    Form factor functions for range of scatterer sizes are often stored in LUT
  Proportional to FT of the autocorrelation function of acoustic impedance within a medium
In addition to Faran model, more simplified models used for form factor analysis include fluid sphere, spherical shell, and Gaussian models

## Slide 7
Commonly assumptions:
  Discrete scatterers within uniform background
  Tissue homogeneity
  Backscattering echoes generated from weakly stationary process
  Behavior with frequency solely dependent on size
For experimental form factor data, assumes that scatterers within ROI are of single size
  Single scatterer size may not offer enough insight into structure
  However, can also describe continuum of scatterer sizes via simple Gaussian or exponential distributions
Scatterer size estimates are bandwidth and fc dependent (generates a bias)
  Susceptible to noise in spectral estimates due to oscillatory behavior of form factor
  Larger bandwidth makes fit more robust to noise
Backscattered signal is attenuation dependent (local variations will affect scatterer size prediction)
Notes: Not often the case for tissue in vivo, especially cancerous tissue

## Slide 8
Form factor to find Effective Scatterer Diameter (ESD)
Spectral slope (SS)
Backscatter coefficient (BSC)